## Slide 1: Starting from the bottom: Coupling a genetic algorithm and a pore network model for porous electrode design Maxime van der Heijden, Rik van Gorp, Gabor Szendrei, Victor de Haas, Mohammad Amin Sadeghi, Jeffrey Gostick, and Antoni Forner Cuenca
234th ECS Meeting
May 28th, 2023

## Slide 2: Redox flow batteries for large-scale energy storage
Rechargeable
Decoupled energy (tank size) and power (reactor size): upscaling possibilities
Currently too expensive
Anode
Cathode
A(n-1)+
An+
A(n-1)+
An+
Membrane
Ions
Ions
Load
Current collector
e-
e-
Catholyte
Anolyte
Pump
Pump

## Slide 3: Porous electrode engineering is a complex multiscale optimization problem
100
A(n-1)+  An+ + e-
Anode
Cathode
A(n-1)+
An+
A(n-1)+
An+
Membrane
Ions
Ions
Load
Current collector
e-
e-
Catholyte
Anolyte
Pump
Pump
Key properties:
Surface area ↑
Mass transport ↑
Pressure drop ↓
Mechanical properties ↑
Electrochemical activity ↑
(Electro)chemical stability ↑

## Slide 4: Tailored electrodes for all-liquid systems
Current generation not optimized, affecting three major losses:
Activation losses
Ohmic losses
Mass transport losses
Hierarchical organization
↓ Pressure drop
↑ Electrochemical performance
200 μm

## Slide 5: Bottom-up design of porous electrodes
Experimental
characterization
Pore network
model
Genetic
optimization
Advanced
manufacturing
Device
implementation
Battery tests
Chemistries
Imaging
Network extraction
Pore simulations
Parameter analysis
Bottom-up
Theory of evolution
Self-evolving
3D printing
Phase separation
Carbonization
Post-treatment
Durability
Cost analysis

## Slide 6
Initial population
Scaling
Initial network
System and parameter selection
Termination criterion
Fitness function
Electrochemical PNM
Crossover
Mutation
Merging and splitting
Selection
Termination
Fe3+
Fe2+
VO2+
VO2+
FTFF
IDFF
Chemistry
System and parameter selection
Initial network
Initial population
Iterative algorithm
Developing a genetic algorithm using the theory of evolution
Cubic
Extracted

## Slide 7
Initial population
Scaling
Initial network
System and parameter selection
Termination criterion
Fitness function
Electrochemical PNM
Crossover
Mutation
Merging and splitting
Selection
Termination
Anode
Cathode

Scaling
Electrochemical pore network model
Fitness function
Termination
Genetic evolution using a pore network model
= 1000 ?

## Slide 8
Initial population
Scaling
Initial network
System and parameter selection
Termination criterion
Fitness function
Electrochemical PNM
Crossover
Mutation
Merging and splitting
Selection
Termination
Selection
Crossover
Mutation
Merging and splitting
or
Iterative genetic algorithm scheme using the theory of evolution
= 1000

## Slide 9
Initial population
Scaling
Initial network
System and parameter selection
Termination criterion
Fitness function
Electrochemical PNM
Crossover
Mutation
Selection
Termination
Iterative genetic algorithm scheme for proof of principle
Cubic
VO2+
VO2+
Flow through
Chemistry
e-
= 50
= 10
= 1000

## Slide 10: Proof of principle
= 50
= 10
= 1000
= [13x13x4]
0.2 M Vanadium, 0.5 V, 1.5 cm s-1
Fitness
Pumping power, Ppump
Electrical power, Pel
+ 75% Fitness
- 72% Ppump
+ 42% Pel

## Slide 11: Structure evolution
= 50
= 10
= 1000
= [13x13x4]
Generation 0
Generation 999
0 10 20 30 40
Pore diameter [μm]
0 4 8 12 16
Throat radius [μm]
100 μm
Thickness
Membrane
Current collector
Flow direction
0.2 M Vanadium, 0.5 V, 1.5 cm s-1
Can we optimize more realistic structures?

## Slide 12: Towards complex electrode structures
Anode
Cathode
Membrane
An+
A(n-1)+
Load
e-
e-
An+
A(n-1)+
e-
e-
e-

## Slide 13: Incorporating design flexibility by pore merging and splitting
Merging
Splitting
Generation 0
Generation 999
Pore diameter evolution
Generation 0
Generation 999
+ Merging and splitting
Diameter
0 10 20 30 40
Pore diameter [μm]
100 μm
Flow direction
+ 39% Fitness
- 56% Ppump
+ 9% Pel
0.2 M Vanadium, 0.5 V, 1.5 cm s-1

## Slide 14: The evolution of extracted networks
Generation 0
Generation 999
100 μm
Generation 0
Generation 499
Carbon paper
Cubic lattice
Cubic lattice
+ 11% Fitness
- 33% Ppump
+ 0% Pel
0 10 20 30 40
Pore diameter [μm]
X-ray tomography
+
SNOW algorithm
Flow direction
0.2 M Vanadium, 0.5 V, 1.5 cm s-1
Void
Solid

## Slide 15: The influence of flow field induced flow pathways in the electrode
Flow-through flow field
Interdigitated flow field
Inlet
Outlet
Rib
x
y
z
500 μm
80
90
100
Concentration [mol m-3]
Membrane
Inlet
Outlet
Membrane
0
0.1
0.2
Absolute velocity [cm s-1]
0.05
0.15
Membrane
y
z
Outlet
Inlet
Rib
Membrane
Outlet
Inlet
Outlet
Outlet
Inlet
Inlet

## Slide 16: The influence of flow field induced flow pathways on the evolution
Generation 0
Generation 999
Flow-through flow field
Generation 0
Generation 486
Interdigitated flow field
Outlet
Inlet
Rib
Flow direction
100 μm
0 10 20 30 40
Pore diameter [μm]
+ 88% Fitness
- 75% Ppump
+ 24% Pel
0.2 M Vanadium, 0.5 V, 1.5 cm s-1

## Slide 17: Towards complex electrode structures
Anode
Cathode
Membrane
An+
A(n-1)+
Load
e-
e-
An+
A(n-1)+
e-
e-
e-

## Slide 18: The big picture
Experimental
characterization
Pore network
model
Genetic
optimization
Advanced
manufacturing
Device
implementation
+
+
+
500 μm
500 μm

## Slide 19: Acknowledgments
Contact:
m.v.d.heijden@tue.nl